## Slide 1: Stage Report
Tianyu Wang
Sep 19th , 2018
VE490 INDOOR LOCALIZATION

## Slide 2
Contents
Rationale
Basic Concepts
Paper Collection
2
Contents

## Slide 3
3
Rationale
Indoor Localization: locate objects or people inside a building using sensory information collected by mobile devices.
GPS not suitable under this scenario: microwaves attenuated sharply indoor.
Major difficulties:
1. Ranging errors;
2. Dominant NLOS condition;
3. Lack of breakthrough in demanding precision.

## Slide 4
4
Concepts
LOS: direct path from the source to the receiver.
NLOS: reflection, diffraction...due to the existence of obstacles.
Ranging Error: deviation of the measured geometric distance.
Anchors: nodes with known fixed positions.
Access Points: points where relevant information could be collected (position information not necessarily known).
Reference Points: points whose position information known and deliberately selected.

## Slide 5
5
Concepts
Major Existing Techniques could be divided into three categories:
1. Proximity detection;
direct search for the target location by anchor access points
2. Triangulation;
use geometric measurements and analysis, e.g., AOA
3. Scene Analysis;
fingerprinting, e.g., WiFi
generally include offline training and online localization

## Slide 6
6
Concepts
The Characteristics of High-frequency Waves (mmW, THz):
1. Highly-directional: less affected by NLOS condition;
make triangulation more possible and feasible?
2. Large bandwidth: accurate range measurement;
anchors more reliable?
3. Small-sized device
more flexible?

## Slide 7
7
Paper [1]
A Deep Neural Network-Based Indoor Positioning Method using Channel State Information
Department of Electronic Engineering, National Taipei University of Technology, Taipei,
2018 Workshop on Computing, Networking and Communications (CNC)
Model: DNNFi (in comparison to DeepFi model proposed in another paper CSI- Based Fingerprinting for Indoor Localization: A Deep Learning Approach )
Representation: 1 AP, N RPs, 10000 CSI measurements (features a DNN with 10000*N input matrix and N*1 output vector indicating which RP is hit). Offline train DNN and online estimate the target location using the N*1 output as weights for each RP’s locations (weighted sum).
Advantage: Only one model for all the locations; supervised; maximum 2-m error.
Disadvantage: Too many measurements; only one AP;

## Slide 8
8
Paper [2]
CiFi: Deep Convolutional Neural Networks for Indoor Localization with 5GHz Wi-Fi
Department of Electrical and Computer Engineering, Auburn University, Auburn
IEEE ICC 2017 SAC Symposium Big Data Networking Track
Model: focus on the phase difference of different antennas
Representation: 1 AP with 3 antennas, 960 packets, each packet containing 60 CSI phase differences, from antenna 1 and 2, 3 and 4, respectively. These values are used to estimate AOA values. Finally form 16 images with 60*60 size for each location and feed into DCNN for training.
Advantage: new insights into phase information; rich information.
Disadvantage: A maximum error of 5m; computational complexity.